Pioneer 3-AT initial researche

Creator	Adept MobileRobots
Country	United States
Year	1995
Type	Research, Industrial
Body	1.6mm lacquered aluminium body
Wheels	Reinforced tires
Weight	12kg
Maximum payload (level surface)	12kg
Maximum payload (grass, mud)	10kg
Maximum payload (asphalt)	5kg
	Skid steering drive
Turn radius	0cm
Swing radius	34cm
Max speed	0.7m/s
Rotation speed	140 degrees/s
Max. Traversable step	10cm
Max. Traversable gap	15cm
Max. Traversable grade	35%
Traversable terrain	Asphalt / Flooring / Sand / Mud(tires available for indoor use)
Autonomy	2-4 hours with 3 batteries (with no accessories)
Charge time	12 hours (standard) or 2 hours (optional high-capacity charger)
Supply voltage	5V @ 1.5A; 12V @ 2.5A
	Hot swappable batteries
	Up to 312 V 7.12 Ah lead acid batteries
Available recharge options	Direct plug-in / Powercube (3-battery charging bay)
Micrcontroller I/O	32 digital inputs / 8 digital outputs / 7 analogue inputs / 3 serial expansion ports
User control panel	MIDI programmable piezoelectric buzzer / Power indicator / Battery recharge indicator / 2 AUX power switches / Reset / Motor enable push-button

According to Adept mobilerobotics, Pioneer robots are a standard in intelligent mobile platforms. The pioneer robot core software is includede with all research platforms such as ARIA, MobileSim, MobileEyes, Mapper 3 Basic and SONARNL. The Pioneer robot can be used with laser-range finders, mono- and stereo-vision cameras, front and rear SONAR arrays and many more other optional accessories.

Bibliography

Generation robots. (No publishing date available). Pioneer 3-AT mobile robot. Available at https://www.generationrobots.com/en/402397-robot-mobile-pioneer-3-at.html. Accessed 21 September 2019.

IEEE. (No publishing date available). Pioneer 3. Available at https://robots.ieee.org/robots/pioneer. Accessed 21 September 2019.

Adept mobilerobots. (No publishing date available). Pioneer 3-AT.